## Slide 1: VibraCom: Vibratory Communication in Smart Devices
Project Members: Asmit De, Shruti Mohanty, Karthikeyan Nagarajan
Professor: Dr. Mahanth Gowda
CSE 597 Project Presentation

## Slide 2
Introduction and Problem Statement
Solution Platform
VibraCom Design
  Data Transfer Using Vibrations
VibraCom Data Detection & Analysis
  Raw Vibration Data
  Envelope Application
  Clean Output Generation
  Encoded Message Extraction
Outline
CSE 597 Project
2
Performance Evaluation
  Error Rate
  Throughput
  Robustness to Multiple Data Patterns
Conclusions
  Applications
  Limitations

## Slide 3
Goal: Investigate the possibility of communicating using vibrations, specifically between a user’s finger and a mobile phone.
How: Leverage techniques shown in [1] and [2] to transfer encoded binary data to a receiving smartphone.
Key Challenges:
  Low accuracy and reliability due to use of smartphone in-built vibration motors, accelerometers, and microphones.
  Low SNR: Detect and extract relevant information from very noisy sensor data.
  Design space exploration to improve throughput and accuracy of the system.
  Explore data transfer through human bone.
[1] Roy, Nirupam, Mahanth Gowda, and Romit Roy Choudhury. "Ripple: Communicating through physical vibration." 12th {USENIX} Symposium on Networked Systems Design and Implementation ({NSDI} 15). 2015.
[2] Roy, Nirupam, and Romit Roy Choudhury. "Ripple {II}: Faster Communication through Physical Vibration." 13th {USENIX} Symposium on Networked Systems Design and Implementation ({NSDI} 16). 2016.
Introduction & Problem Statement
CSE 597 Project
3

## Slide 4: Evaluation Platform
Android OS and sensor APIs
Smartphone haptic motors for transmitting data signals
Smartphone IMUs for receiving encoded data signals
Human body as the communication channel
Smartphone mics for side-channel exploration
CSE 597 Project
4

## Slide 5: VibraCom Design
Vibration → Change in accelerometer Reading
Three key operations:
  Vibration Control
  Accelerometer Data Sensing
  Data Analysis/Message Extraction
CSE 597 Project
5
[2]

## Slide 6: VibraCom Operations
CSE 597 Project
6
Vibrations
Generated
Vibrations
Sensed
Vibrations
Decoded!

## Slide 7: Data Analysis of Accelerometer Data
CSE 597 Project
7
1
0
1
0
1
0
1
0
1
0
Message?
Envelope Function
Sq. Wave Gen.

## Slide 8: Accelerometer Challenges
Each bit requires ~2 seconds to be sensed accurately.
  Noise
  Sampling Rate
Bone Conduction
  Damping Effect
  Low Vibration Amplitude → Low SNR
Solution?
  Need for alternate sensing method.
  Ripple II [2] uses acoustic sensing of vibration using the smartphone microphone.
CSE 597 Project
8

## Slide 9: Data Analysis of Microphone Data
CSE 597 Project
9
Message?
Envelope Function
Sq. Wave Gen.
1
0
1
0
0
1
0
0
1
0

## Slide 10: Discussion
Throughput
  Accelerometer: 0.5 bps
  Microphone: 20 bps
Accelerometer readings depend on the sampling rate
  High accuracy provides ~5 samples/s.
  Medium accuracy provides ~15 samples/s.
Accelerometer: Unreliable when 1 bit represented by <2s vibration.
  Accuracy = 67%
Microphone: ~99% accurate when 1 bit represented in ~0.1s of vibration.
CSE 597 Project
10

## Slide 11: Evaluation
Since we are transferring a password, it is essential to minimize the BER.
Transmitting at a higher Bit Rate (BR) might increase the BER.
Lab of Green and secure Integrated Circuit Systems (LOGICS)
5
CSE 597 Project
11

## Slide 12: Applications
Vibratory ring worn by user can transfer encoded passwords to smartphones for a secure single factor authentication.
Can be used as a security key for 2-Factor Authentication (2FA).
Can be used in conjunction with PINs for payment authorizations.
Can be used to send data between two on-body smart devices securely via vibrations instead of insecure wireless channels.
CSE 597 Project
12

## Slide 13: Conclusions
Low Bit rate for accelerometer-based VibraCom.
On-body vibratory communication was unsuccessful.
  Can be mitigated with high amplitude motors or high precision accelerometers.
  Microphone-based VibraCom can be used if receiving device is held in hand.
Requires a preamble/header to identify transmission of data.
  Ex. We used a 2-bit preamble of ’10’.
Microphone-based VibraCom is limited to <5cm proximity between communicating devices.
  Beneficial to prevent acoustic side channels.
CSE 597 Project
13

## Slide 14
Thank You!